## Slide 1: Team 5 Conceptual Design
Dillon Williams
Nidhay Patel
Ryan Reed
Michel Turpeau
Austin Sigg

## Slide 4: Microcontroller
Raspberry Pi Model 4 B
  Card Reader
    Input: Signal/Message/Information from Eagle Card
    Output: Create Data and signal Microcontroller Unit
  UI
    Raspberry Pi LCD touchscreen
      Input: Information from Student
      Output: Raspberry Pi signaling PLC

## Slide 5: Pi connections
Raspberry Pi
SQL Database
Touchscreen
Eagle Card Reader
Ethernet

## Slide 6: SQL Database
Inventory
  Loaded
  Unloaded
Student Information
  T#
  Name
  Email
  Course & Board#
Ethernet
  CSV File

## Slide 7: Hardware connections
PLC
HW Control
  Locks
  Indication
  Timer System
  Sensors (Addressed later)
  Motor

## Slide 8: Why a plc & a microcomputer?
PLC’s “run-to-completion” step is Cycle-Driven!
  Will always scan its code on a given interval (ex. every 100ms)
  A microcomputer is event-driven: will complete its scan once an event is activated
    Could be SIGNIFICANTLY longer
PLCs are used in industry specifically for control technology
  Almost all hardware in industry can be easily controlled by PLCs
  Makes controlling fewer components much more simple
If PLCs can do this, why not use it for a database?
  PLCs aren’t good with sharing a lot of data, except for HMIs and DAQs
  Can’t understand SQL

## Slide 9: Plc Control / Hardware
PLC Constraints
  ii(1) Must interface with the locks and LEDs
  ii(2) Must control the step voltage of the motor(s)
  ii(3) Must communicate with the microcomputer
  ii(4) Must know the device occupancy of each drawer
  ii(5) Must have a timer system
Hardware
  PLC receives power from wall outlet
  Hardware receives all control from the PLC
  Sensors, Locks, Timer System, Indication System, Motor

## Slide 10: Hardware subsystems
Stepper Motor
  PLC will control driver for motor
  Motor steps enough degrees to rotate new device to drawer
Locks
  Most likely solenoid (Proposed by MechE team)
  Powered by DC voltage
Indication System
  Most likely LEDs. Will help guide student to correct drawer and compartment
  Controlled by PLC
Timer System
  Used to flash LEDs and unlock compartments over a predetermined duration
  Controlled by PLC
  Will be a system to alternate TON timers

## Slide 11: Explanation for Stepper Motor

## Slide 12: Locks
Main security for the physical system.
Locks for each of the drawer, and for each of the compartments.
The drawers will require more strength, since they are directly exposed and easy to grab a hold of.
Needs to stay lock when power is lost.

## Slide 13: LEDs and Indicators
To assist the user, both the operator and the consumer, there will be a series of LED indicators guiding them to the designated compartment.
User Mode (For Consumer):
  After successfully completing the rental process the LED will flash, indicating the drawer and the compartment that the item is stored.
  Once the item is removed and the compartment and drawer are closed, the LEDs turn off.

## Slide 14: Barcode Scanner
Used to scan in the ID/barcode attached to the device’s box.
Makes it easy to keep track of items have been registered to the database.
Will be used by the operator during the “LOAD” mode.

## Slide 15: LOAD Mode
Mode loading and registering items to the machine.
The machine is aware of empty compartment.
LED indicators will inform the user of the compartment that needs a new item. (The only ones unlocked)
The user CANNOT move on to the next drawer until they have scanned in the device and loaded it into its compartment.

## Slide 16: Power
Power Supply
AC/DC Converter
Overcurrent Protection
  GFCI-protected outlet
    NEC 422.51
    Circuit Breaker
    Fuses
Op-Amp Circuits
Constraints:
iv(1) As per the standard NEC 422.51, the power system must have a ground fault current interrupter (GFCI) to protect against the current surge.
iv(2) The power system must have an AC/DC converter to send power to the voltage-sensitive components.
iv(3) The power system must have an emergency stop control.

## Slide 17: Systems that require Power
Microcomputer
PLC
Motor
LEDs
Locks
Barcode Scanner
Card Reader

## Slide 18: Sensors
To determine occupancy of each compartment
Hundreds of options to consider
Ideals
  Small Size
  One bit output
  Cheap
  Easy Calibration
Constraints: iii(4) The PLC must know the device occupancy of each drawer.