## Slide 1: Team 5 Conceptual Design
Dillon Williams
Nidhay Patel
Ryan Reed
Michel Turpeau
Austin Sigg

## Slide 3: Microcontroller
Raspberry Pi Model 4 B
  Card Reader
    Input: Signal/Message/Information from Eagle Card
    Output: Create Data and signal Microcontroller Unit
  UI
    Raspberry Pi LCD touchscreen
      Input: Information from Student
      Output: Raspberry Pi signaling PLC

## Slide 4: Pi connections
Raspberry Pi
SQL Database
Touchscreen
Eagle Card Reader
Ethernet

## Slide 5: SQL Database
Inventory
  Loaded
  Unloaded
Student Information
  T#
  Name
  Email
  Course & Board#
Ethernet
  CSV File

## Slide 6: Hardware connections
PLC
HW Control
  UI
  Locks
  Indication
  Timer System
  Sensors (Addressed later)

## Slide 7: Plc / Control
PLC
  Powered from wall outlet
  Outputs to Control
Control
  Hardware control
  Outputs to Sensors, UI, Locks, Timer System, Indication System

## Slide 8: Hardware subsystems
UI
  Communicates with Pi and PLC to create display and store info in database
Locks
  Most likely solenoid (Proposed by MechE team)
  Powered by DC voltage
Indication System
  Most likey LEDs. Will help guide student to correct drawer and compartment
  Controlled by PLC
Timer System
  Used to flash LEDs and unlock compartments over a predetermined duration
  Controlled by PLC

## Slide 9: Barcode Scanner
Used to scan in the ID/barcode attached to the device’s box.
Makes it easy to keep track of items have been registered to the database.
Will be used by the operator during the “LOAD” mode.

## Slide 10: Locks
Main security for the physical system.
Locks for each of the drawer, and for each of the compartments.
The drawers will require more strength, since they are directly exposed and easy to grab a hold of.
Needs to stay lock when power is lost.

## Slide 11: LEDs and Indicators
To assist the user, both the operator and the consumer, there will be a series of LED indicators guiding them to the designated compartment.
User Mode (For Consumer):
  After successfully completing the rental process the LED will flash, indicating the drawer and the compartment that the item is stored.
  Once the item is removed and the compartment and drawer are closed, the LEDs turn off.

## Slide 12: LOAD Mode
Mode loading and registering items to the machine.
The machine is aware of empty compartment.
LED indicators will inform the user of the compartment that needs a new item. (The only ones unlocked)
The user CANNOT move on to the next drawer until they have scanned in the device and loaded it into its compartment.

## Slide 13: Power
Power Supply
AC/DC Converter
Step Down Transformer
Op-Amp Circuit

## Slide 14: Systems that require Power
Raspberry Pi
Barcode Scanner
PLC
Locks
Card Reader

## Slide 15: Sensors
To determine stock of each compartment
Considerations:
  Photo Eye Light Sensor
  Scale Weight Sensor