## Slide 1: Team 5 Conceptual Design
Dillon Williams
Nidhay Patel
Ryan Reed
Michel Turpeau
Austin Sigg

## Slide 2: Design Update
More like Barrel shape
  Motor at Bottom
  Each level will have lock
  LEDs to guide

## Slide 4: Constraints
Engineering Standards
National Electric Safety Code
  High Voltage Components
  Multiple Sensors and Wires
  Power system must have GFCI (NEC 422.51)
Ethical Considerations
Prevent from Stealing Devices
Safety of Students when checking out device
Broader Impacts
Not to take away jobs of Office Associates
  Job simplified
  Less paperwork
|||||||||
|
|
|
|
|
|
|
|
|

## Slide 5: Microcomputer system
To hold Database
Must have Connectivity Ports
Also responsible for sending & receiving information/signal
  UI
    LCD Touchscreen to collect student information
    Select Board to Vend

## Slide 6: PC connections
miniPC
SQL Database
Touchscreen
Eagle Card Reader
Ethernet
USB

## Slide 7: SQL Database
Inventory
  Loaded
  Unloaded
Student Information
  T#
  Name
  Email
  Course & Board#
Ethernet
  CSV File

## Slide 8: Constraints
USB
Be able to automatically transfer data to the faculty’s thumb drive when inserted into the machine
Database
Have a created Schema available and have a server to contain the student data and Schema itself
Card Scanner
Be able to read data from Eagle Cards and store the identifier in the database for faculty use

## Slide 9: Hardware connections
PLC
HW Control
  Locks
  Indication
  Timer System
  Sensors (Addressed later)
  Motor

## Slide 10: Why a plc & a microcomputer?
PLC’s “run-to-completion” step is Cycle-Driven!
  Will always scan code on set interval (ex. every 100ms)
  A microcomputer is event-driven: will complete its scan once an event is activated
    Could be SIGNIFICANTLY longer
PLCs are used in industry specifically for control technology
  Hardware in industry usually controlled by PLCs
If PLCs can do this, why not use it for a database?
  PLCs aren’t good with sharing a lot of data
  Can’t understand SQL

## Slide 11: Plc Control / Hardware
PLC Constraints
  ii(1) Must interface with the locks and LEDs
  ii(2) Must control the step voltage of the motor(s)
  ii(3) Must communicate with the microcomputer
  ii(4) Must know the device occupancy of each drawer
  ii(5) Must have a timer system
Hardware
  PLC receives power from wall outlet
  Hardware receives all control from the PLC
  Sensors, Locks, Timer System, Indication System, Motor

## Slide 12: Hardware subsystems
Stepper Motor
  PLC will control driver for motor
  Motor steps enough degrees to rotate new device to drawer
Locks
  Most likely solenoid (Proposed by MechE team)
  Powered by DC voltage
Indication System
  Most likely LEDs. Will help guide student to correct drawer and compartment
  Controlled by PLC
Timer System
  Used to flash LEDs and unlock compartments over a predetermined duration
  Controlled by PLC
  Will be a system to alternate TON timers

## Slide 13: Explanation for Stepper Motor
Stepper Motors are DC motors that divide a full rotation into a set of equal steps.
This will allow us to have better control over the positioning of the machine.

## Slide 14: Rotation System

## Slide 15: Motor Driver
This motor driver uses a closed-loop system
This improves the accuracy of the motor and makes it so it never loses track of it step.
This driver also includes over-current, over-voltage and position ultra difference protection

## Slide 16: Locks
Main security for the physical system.
There are locks for each of the compartments and another for the storage/maintenance space.
Needs to stay lock when power is lost.

## Slide 17: LEDs and Indicators
There are 3 compartments, one for each level.
The LED will show the user the location of their device.

## Slide 18: Barcode Scanner
Used to scan in the ID/barcode attached to the device’s box.
Makes it easy to keep track of items have been registered to the database.
Will be used by the operator during the “LOAD” mode.

## Slide 19: LOAD Mode (Button Included)
Mode for loading and registering items to the machine.
The display will inform the user of the compartment, indicated by an LED, that needs a refill. (The only one unlocked)
The operator will scan the ID of the device and load it into position.
After a confirmation of the board being loaded, the machine will automatically rotate to the next empty slot.

## Slide 20: Power
Power Supply
AC/DC Converter
Overcurrent Protection
  GFCI-protected outlet
    NEC 422.51
    Circuit Breaker
    Fuses
Op-Amp Circuits
Constraints:
iv(1) As per the standard NEC 422.51, the power system must have a ground fault current interrupter (GFCI) to protect against the current surge.
iv(2) The power system must have an AC/DC converter to send power to the voltage-sensitive components.
iv(3) The power system must have an emergency stop control.

## Slide 21: Systems that require Power
Microcomputer
PLC
Motor
LEDs
Locks
Barcode Scanner
Card Reader

## Slide 22: Sensors
To determine occupancy of each compartment
Hundreds of options to consider
Ideals
  Small Size
  One bit output
  Cheap
  Easy Calibration
Constraints: iii(4) The PLC must know the device occupancy of each drawer.